## Slide 1
HANDOVER PROBABLITY IN DRONE CELLULAR NETWORK
CSE 400 : s1_g14_net
Motivation :
  Drone Base Stations (DBSs) can provide temporary wireless coverage.
  In drone networks, base stations move instead of users.
  Movement causes frequent topology changes.
  Even a static user may experience handovers.
  System contains uncertainty due to:
1. random drone locations
2. random speeds
3. random movement directions
  Goal: analyze handover behavior using simulation.

## Slide 2
Objective :
  Simulate drone cellular network.
  Compute probability of handover before time t .
P(H(t)) = Probability that serving drone changes before time t
Deterministic baseline strategy :
  User always connects to nearest drone.
  No randomness in association rule.
  Same rule used in reference paper.
Why reasonable :
  Standard rule in cellular networks.
  Used in theoretical analysis.
  Allows study of mobility effects only.
Project Objective and Deterministic Baseline

## Slide 3
System Pipeline Overview
Simulation pipeline:
  Generate drone locations using Poisson Point Process.
  Select nearest drone as serving drone.
  Assign random speed and direction.
  Move drones for time t.
  Recalculate distances from user.
  Detect handover event.
  Monte-Carlo simulation – compute density and handover probability.
Where uncertainty enters:
  (PPP) drone deployment
  speed distribution
  movement direction
PPP Deployment
Select Serving Drone
Assign Speed & Direction
Move Drones
Distance Calculation
Handover Check
Monte-Carlo Simulation & Results

## Slide 4
Sources of Uncertainty
Simulation method:
  Monte-Carlo simulation
  Multiple realizations
  Average over all results
How uncertainty is handled
Purpose
Sources
  Model realistic mobile network.
  Compute Density and handover Probability
  PPP distribution of drones
  Random number of drones
  Random speed of drones
(Speed follow a probability distribution rayleigh/uniform)
  Random movement direction
Uncertainty comes from stochastic modeling.

## Slide 5
Variable | Meaning | Distribution
N | number of drones | Poisson
 | drone position | Uniform in region
 | drone speed | Rayleigh / Uniform
 | movement direction | Uniform (0, 2π)
 | distance to serving drone | random
 | distance to non-serving drone | random
Key Random Variables
These variables determine:
  drone movement
  density evolution
  handover event
The simulation uses random variables to model drone mobility.

## Slide 6
Drone locations follow PPP : ΦD ∼ PPP(λ0)
Drone speed is random : V∼fv(v)
Movement direction is random : θ∼U(0,2π)
Deterministic baseline rule:
  User always connects to nearest drone
  No randomness in association decision
Probabilistic Modeling with Deterministic Decisions
Handover event:
H(t)={∃ drone closer than serving drone}
So:
  environment random
  decision rule is fixed
Assumptions used in simulation:

## Slide 7
The system uses a deterministic baseline association strategy in which the user always connects to the nearest drone base station.
Nearest–neighbor association rule:
  Φ = set of drone base stations
  o = user location
  x* = serving drone
Logic behind deterministic baseline:
  The nearest drone provides the strongest average signal.
  This rule is commonly used in cellular network analysis.
  It allows tractable modeling using stochastic geometry.
  It ensures that randomness comes only from drone mobility.
Therefore, the deterministic baseline is used as a reference model
to study the effect of drone movement on handover probability.
Deterministic Baseline Logic

## Slide 8
Simulation Implementation
Simulation was implemented in Python based on the reference paper.
The original MATLAB simulation code was converted to Python and executed.
Two simulation modules were used:
  Density simulation
    Computes density of non-serving drone base stations over time
  Handover simulation
    Computes probability of handover for different time values
Implementation of Density Simulation:
  Change speed parameters and use 3 different variations - 45kmh, 60kmh and 80kmh
  Run simulation
  Generate plots for density
  Compare results with theoretical expressions
Implementation of Handover Simulation:
  Implemented the simulation setup for both mobility scenarios: SSM and DSM.
  Run simulation
  Generate plots for density
  Compare results with theoretical expressions

## Slide 9
Results and Performance Analysis : Density Simulation
Speed 45 km/hr

## Slide 10
Results and Performance Analysis : Density Simulation
Speed 60 km/hr

## Slide 11
Results and Performance Analysis : Density Simulation
Speed 80 km/hr

## Slide 12
Results and Performance Analysis : Handover Simulation
1,00,000 Simulations

## Slide 13
Nearest-drone rule limitations:
  ignores signal strength
  ignores interference
  ignores network load
  sensitive to mobility
High speed → many handovers
High density → more switching
Need smarter strategies.
Limitations of Deterministic Strategy

## Slide 14
Summary and Transition to Randomized Strategies
Summary:
  Drone network modeled using stochastic geometry.
  Simulation used to verify theory.
  Density and handover probability computed.
  Deterministic nearest-drone rule used.
Observation:
  mobility increases handovers
  deterministic rule not always optimal
Future work:
  adaptive association
  probabilistic strategy
  mobility-aware selection